## Slide 1: Mirage Cores: The Illusion of Many Out-of-order Cores Using In-order Hardware
Shruti Padmanabha, Andrew Lukefahr*, Reetuparna Das, Scott Mahlke
Micro-50, Boston
Oct 18, 2017
University of Michigan
Electrical Engineering and Computer Science
*Now at Indiana University

## Slide 2: General purpose computer architectures
Single-thread
performance
System
throughput
Energy
efficiency

## Slide 3: Heterogeneous CMP architectures
Out-of-order Core
High performance
Dynamically reorders instructions
Large, complex, one-size fits all design
Low energy efficiency
OoO
CMP Area
Single-thread
performance
System
throughput
Energy
efficiency

## Slide 4: Heterogeneous CMP architectures
OoO
Chip Area
InO
In-Order Core
Smaller, simplistic design
Low area
Low power
Issues instructions in program order
Low performance
Single-thread
performance
System
throughput
Energy
efficiency

## Slide 5: Heterogeneous CMP architectures
OoO
Chip Area
OoO
InO
InO
InO
InO
InO
InO
InO
InO
Single-thread
performance
System
throughput
Energy
efficiency

## Slide 6: Mirage Cores - Objective
Single-thread
performance
System
throughput
Energy
efficiency
More cores
More InO cores
More OoO-like InO cores

## Slide 7: Background: DynaMOS “More OoO-like InO cores”
InO
Program
Traces
OoO
Sched$
Memoize!
OinO HW
  OinO vs InO
  Performance: 1.4X
  Area: 1.2X
  Energy: 1.4X
  70% of the traces have equivalent schedules for most of their lifetimes
Notes: More overhead details in the paper

## Slide 8: Mirage Cores: Motivations
Memoization opportunities vary based on program/phase characteristics
  InO cores can utilize memoized traces for phases of millions of instructions
OinO
OinO
OinO
OoO
OinO
Notes: Bzip and astar

## Slide 9: Mirage Cores: Concept
InO
InO
InO
InO
OoO
Chip Area
OoO
OoO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
OoO+
Schedule producer
Single-thread
performance
System
throughput
Energy
efficiency

## Slide 10: Mirage Cores: Challenges
Efficiently time-share the OoO
Architecture
  # OinOs per OoO
  Minimize overheads
Effectively arbitrate between applications
  Metrics?
  Goals?
OoO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
OoO+
Schedule producer
Notes: 1. Benefits : we need to find a good

## Slide 11: Mirage Cores: Architecture
Arbitrator
InO+OinO
OoO
Sched$
L1i$
L1d$
Interconnect
To Shared L2
To Shared L2
Sched$
L1i$
L1d$
InO+OinO
Sched$
L1i$
L1d$
InO+OinO
Sched$
L1i$
L1d$
InO+OinO
Sched$
L1i$
L1d$
…

## Slide 12: Arbitration Between Applications
Arbitrator
App1
App2
App3
OoO Candidate
App0
Execution
metrics
Time
…
1 Million cycles
App0
??
Notes: Note that we have 4 apps running, while the ooo is waiting for the next app to memoize for

## Slide 13: Metrics for arbitration
Execution metric | Determines | Measure
Memoizability | Single-application speedup | ∆Sched$-MPKI

## Slide 14: Memoizability - ∆Sched$-MPKI
Relationship between performance and Sched$-MPKI for bzip2
Program in increasing order of 1M cycle intervals
Memoization
delta =
..
IPC
∆Sched$-MPKI
.

## Slide 15: Metrics for arbitration
Execution metric | Determines | Measure
Time on OoO | Fairness | 
Time on OoO | Fairness | 
Slowdown | System throughput | Slowdown =
Slowdown | System throughput | 
Memoizability | Single-application speedup | ∆Sched$-MPKI

## Slide 16: Goals for arbitration
Maximize energy efficiency
OoO
OoO
OoO
2. Maximize system throughput
3. Guarantee fair/priority based resource allocation
Traditional Heterogeneous CMP
Notes: These can be combined

## Slide 17: Evaluation Methodology
Architectural Feature | Parameters
OoO Core | 3 wide O3 @ 2GHz 12 stage pipeline 128 ROB Entries 128 entry PRF, 32 entry LSQ
InO Core | 3 wide InOrder @ 2GHz 8 stage pipeline 128 entry PRF, 32 entry LSQ
Memory System | 32 KB L1 i/d cache, 2 cycle access 8KB Schedule cache, 1 cycle access 1MB L2 cache, 15 cycle access 1GB Main Mem, 100 cycle access
Simulator | Gem5
Energy Model | McPAT

## Slide 18: Evaluation
Experimental parameters | Parameters
Number of cores | n-InO + 1 OoO
Baseline | n-OoO
Workloads | Random mixes of n-benchmarks from spec2k6 Each run for a 1 billion instruction simpoint

## Slide 19
Architectures for comparison
OoO
OoO
OoO
OoO
OoO
OoO
OoO
OoO
Homogeneous OoO
CMP
InO
InO
InO
InO
InO
InO
InO
InO
Homogeneous InO
CMP
8:1 configuration
OoO
(booster)
InO
InO
InO
InO
InO
InO
InO
InO
Traditional
Heterogeneous CMP
OoO +
Sched
Producer
OInO
OInO
OInO
OInO
OInO
OInO
OInO
OInO
Mirage Core CMP
Notes: Overall it’s still lesser than ooo homo
But can it keep up with its perf
In our eval we compare against the following cmps

## Slide 20
Chart: Energy Rel to Homo-OoO
46.56% | 0.39825 | 0.45655
Mirage Cores
Traditional Het-CMP
(no memoization)
Chart: Performance Rel to Homo-OoO
Performance | 0.65615 | 0.84104
Homo-InO
Homo-InO
App4
App3
App1
App2
App7
App6
App0
App5
8 InOs with 1 OoO
Homo-OoO
Homo-OoO
  54% energy savings over homogeneous OoO CMP with 16% STP loss
  OR
  24% STP gains over homogeneous InO CMP with 14% energy overhead
Notes: Another way to think about it

## Slide 21: Size of cluster
Chart: Perforamnce Relative to Homo-OoO
| 4.0 | 8.0 | 12.0 | 16.0
maxSTP | 0.70744 | 0.65615 | 0.63108 | 0.61669
SC-MPKI | 0.82904 | 0.84104 | 0.85225 | 0.84118
Chart: Utilization of OoO
| 4.0 | 8.0 | 12.0 | 16.0
maxSTP | 0.98764 | 1 | 1 | 1
SC-MPKI | 0.33496 | 0.59388 | 0.92662 | 0.98564
Number of OinO cores per OoO
  OoO is oversubscribed for n >=12
Homo-InO
Mirage Cores
Traditional Het-CMP
(no memoization)
Homo-OoO

## Slide 22: Conclusion
OoO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
InO+OinO
OoO+
Schedule producer
Reordered
schedules
Achieve > 80% of a homogeneous OoO CMP with > 20% area and > 50% energy savings
Single-thread
performance
System
throughput
Energy
efficiency

## Slide 23: Mirage Cores: The Illusion of Many Out-of-order Cores Using In-order Hardware
Shruti Padmanabha, Andrew Lukefahr, Reetuparna Das, Scott Mahlke
Micro-50, Boston
Oct 18, 2017
University of Michigan
Electrical Engineering and Computer Science
Questions?