## Slide 1
Scalpel: Customizing DNN Pruning to the
Underlying Hardware Parallelism
Jiecao Yu1, Andrew Lukefahr1, David Palframan2, Ganesh Dasika2,
Reetuparna Das1, Scott Mahlke1
1 University of Michigan – Ann Arbor 2 ARM Research
ISCA, June 28, 2017
Notes: Thanks for the introduction. Hi everyone, today, I am presenting my work scalpel: customizing DNN pruning to the underlying hardware parallelism.

## Slide 2
Deep Neural Networks
High storage and computation cost
  AlexNet: 240 MB, 1.5 GFLOP
  VGG: 550 MB, 30.9 GFLOP
DNN compression is necessary
  Removing unimportant parameters
Notes: Deep neural networks are utilized in various applications. A typical DNN includes multiple convolutional layers and fully-connected layers. For fully-connected layers, they can be considered as 1-d vectors. For convolutional layers, they consist of a stack of 2D matrices named feature maps. To achieve a good accuracy, DNNs usually have a large storage size and a high computation cost. As an example, AlexNet has a size of 240MB and needs 1.5Giga FLOPs. Therefore, to employ DNNs in real applications, it is necessary to compress them by removing unimportant parameters in the network.

## Slide 3
DNN Architecture
0 | 0 | 6 | 4 | 0 | 1
2 | 0 | 0 | 3 | 5 | 7
0 | 1 | 2 | 0 | 8 | 0
8 | 0 | 4 | 3 | 0 | 0
0 | 0 | 0 | 0 | 0 | 2
5 | 9 | 1 | 0 | 0 | 1
X
Input Vector
Weight Matrix
=
Output Vector
High redundancy
Notes: This figure shows a fully-connected neural network. Each neuron is connected to all neurons in the previous layer. It combines its weighted inputs to generate the output. For each layer, in the real computation, we will put all weights into a weight matrix. Then this matrix will time with the input vector to generate the outputs. Therefore, the fully-connected layers actually perform the matrix-vector multiplication. In the weight matrix, you can find lots of zeros and weights close to zero. These weights can be considered as the redundancy inside the neural network because they don’t have much impact on the output vector.

## Slide 4
0 | 0 | 6 | 4 | 0 | 1
2 | 0 | 0 | 3 | 5 | 7
0 | 1 | 2 | 0 | 8 | 0
8 | 0 | 4 | 3 | 0 | 0
0 | 0 | 0 | 0 | 0 | 2
5 | 9 | 1 | 0 | 0 | 1
Weight Pruning *
|Weights| > Threshold
* Han, Song, et al. "Learning both weights and connections for efficient neural network." NIPS. 2015.
Weight Matrix
0 | 0 | 6 | 4 | 0 | 1
2 | 0 | 0 | 3 | 5 | 7
0 | 1 | 2 | 0 | 8 | 0
8 | 0 | 4 | 3 | 0 | 0
0 | 0 | 0 | 0 | 0 | 2
5 | 9 | 1 | 0 | 0 | 1
 |  | 6 | 4 |  | 
 |  |  | 3 | 5 | 7
 |  |  |  | 8 | 
8 |  | 4 | 3 |  | 
5 | 9 |  |  |  | 
Computation and storage
Notes: A typical way to remove this redundancy is called weight pruning. We will compare the absolute values of all the weights with a threshold. Only the weights with absolute value higher than the threshold will be kept. Other weights are removed from the weight matrix. After weight pruning, the weight matrix becomes sparse. Since the connections corresponding to the removed weights are also deleted, the network itself will become sparse. By weight pruning, we can remove unnecessary weights and their related computation, which reduces both the computation and storage requirement of DNN models.

## Slide 5
Drawbacks
Sparse format needs extra storage
6 | 4 | 3 | 5 | 7 | 8 | 8 | 4 | 3 | 5 | 9
2 | 3 | 3 | 4 | 5 | 4 | 0 | 2 | 3 | 0 | 1
 |  | 6 | 4 |  | 
 |  |  | 3 | 5 | 7
 |  |  |  | 8 | 
8 |  | 4 | 3 |  | 
5 | 9 |  |  |  | 
CSR Format
A =
JA =
IA =
0 | 2 | 5 | 6 | 9 | 9 | 11
One column index for each weight
Weights
Column indexes
0 | 1 | 2 | 3 | 4 | 5
Notes: However, the sparsity incurred by weight pruning will bring many problems. The first problem is the extra storage of the sparse format. This is the weight matrix we have after weight pruning. It will be stored in the compressed sparse row format which includes three arries. Array A contains all the nonzero weights. Array JA contains the column indexes of the nonzero weights. Array IA records the accumulated number of nonzero weights of each row. As you can see, each nonzero weight needs a column index to record its position. It means the final model of the sparse neural network will spend more than half of the storage to record the sparse format.

## Slide 6
Chart: Relative Model Size, Computation and Exec. Time
| Size | Computation | Time-CPU | Time-GPU
 | 0.22317 | 0.4156 | 1.2475 | 3.3395
Drawbacks
Execution time increase
  Computation reduction not fully utilized
  Extra computation for decoding sparse format
* AlexNet not tested on microcontroller
AlexNet *
Unpruned
Baseline
22%
42%
125%
334%
Notes: The second problem is the execution time increase caused by the sparsity. Weight pruning can reduce the DNN computation by removing redundant weights. But this computation reduction cannot be fully utilized. And the decoding of sparse format also costs extra computation. We test weight pruning on AlexNet and this figure shows the results. The black line here is the unpruned baseline. The first two bars are the relative model size and remaining computation. Both model size and computation are dramatically reduced after weight pruning. The next two bars are the relative execution time on CPU and GPU. As you can see, on both CPU and GPU, the execution time have increased after weight pruning and is much higher than the remaining computation. This figure shows that the sparsity incurred by weight pruning will hurt the DNN computation performance.

## Slide 7
Low parallelism - Micro.
  No cache
  Low storage (~100 KB)
Moderate parallelism - CPU
  ILP / MLP
High parallelism - GPU
  TLP
  High bandwidth / long latency memory
CONV
Scalpel
Trained DNN
Hardware
Parallelism
SIMD-Aware
Weight Pruning
Node Pruning
Layer Type
Pruned DNN
Low
High
Moderate
FC
Notes: To solve these problems, we propose Scalpel. It customize DNN pruning based on different hardware parallelism. The first step is to analyze the level of hardware parallelism. We divide hardware into three categories. The first one is low-parallelism hardware, for example microcontrollers. It has no cache and only small storage. For these hardware, we will apply the SIMD-aware weight pruning. The second category is high-parallelism hardware like GPUs. Thread-level parallelism is utilized, which requires high bandwidth but long latency memory. For these hardware, node pruning will be applied. The third category is the moderate-parallelism hardware, for example desktop CPUs. Instruction-level parallelism and memory-level parallelism are enabled. In this case, we will apply SIMD-aware weight pruning to the fully-connected layers and node pruning to the convolutional layers. After these steps, we can get the pruned DNN models.

## Slide 8
Matrix-Vector Multiplication with SIMD
0 | 0 | 6 | 0 | 5 | 7
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 4 | 0
0 | 0 | 4 | 3 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0 | 0
1
2
1
2
1
1
X
SIMD benefits dense matrix-vector multiplication
0 | 0 | 6 | 0 | 5 | 7
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 4 | 0
0 | 0 | 4 | 3 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0 | 0
Assume SIMD width = 2
  Two loads / multiply-accumulate (MAC) in one instruction
0
1
0
2
x
x
+
+ 0 = 0
6
1
0
2
x
x
+
+ 0 = 6
5
1
7
1
x
x
+
+ 6 = 18
Notes: Before talking about SIMD-aware weight pruning, I will first show an example of how the matrix-vector multiplication is performed with SIMD support. Assume the SIMD width here equals to 2. It means we can perform two loads or two multiply-accumulate operations in one instruction. To generate the first output, we need to time the first row of the weight matrix with the input vector. We will load the first two weights and the corresponding input values. Then two MAC operations can be performed in one instruction to generate the temporary output. After this, we can move to the next two weights to do the computation and so on to get the final output value of 18. As you can see here, the SIMD support can benefit dense matrix-vector multiplication by utilizing the data-level parallelism.

## Slide 9
6
1
x
+ 0 = 6
5
1
x
+ 6 = 11
7
1
x
+ 11 = 18
x
+
x
+
x
+
0 | 1 | 2 | 3 | 4 | 5
Sparse Matrix-Vector Multiplication
0 | 0 | 6 | 0 | 5 | 7
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 4 | 0
0 | 0 | 4 | 3 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 0 | 0
 |  | 6 |  | 5 | 7
 |  |  |  | 4 | 
 |  | 4 | 3 |  | 
 |  | 1 | 2 |  | 
1
2
1
2
1
1
X
6 | 5 | 7 | 4 | 4 | 3 | 1 | 2
2 | 4 | 5 | 4 | 2 | 3 | 2 | 3
Weights
Indexes
SIMD not fully utilized
Extra storage for column indexes
Notes: However, the computation is very different when the weight matrix become sparse. For sparse weight matrix, it will be stored in the CSR format. To perform the computation, we will load the first weight and the first index. The index will then be used to fetch the input value we need to perform the MAC operation to get the temporary output. Then we will go through the next two pairs of weights and indexes to generate the final output. As shown here, the input values we need are not all in continuous addresses. We should use the column indexes to load the input values one by one and perform the related computation. In this case, the computation only needs one of the SIMD units and, therefore, the SIMD support cannot be fully utilized. Also, the index array has the same size with the weights array and it will cost much extra storage space.

## Slide 10
Weights in Groups
0 | 1 | 2 | 3 | 4 | 5
1
2
1
2
1
1
X
 |  | 6 |  | 5 | 7
 |  |  |  | 4 | 
 |  | 4 | 3 |  | 
 |  | 1 | 2 |  | 
 |  | 6 | 0 | 5 | 7
 |  |  |  | 4 | 0
 |  | 4 | 3 |  | 
 |  | 1 | 2 |  | 
6 | 0
5 | 7
4 | 0
4 | 3
1 | 2
Weights
2 | 4 | 4 | 2 | 2
Indexes
6
1
0
2
x
x
+
+ 0 = 6
5
1
7
1
x
x
+
+ 6 = 18
SIMD units fully utilized
Fewer column indexes
Notes: These two problems can be solved by putting weights into aligned groups. Assume now all the remaining weights are in aligned groups. The group width equals to the SIMD width which is 2. Then the weight groups are recorded in the same weight array. But the index array will record only the column index of the first element in each weight group. To perform the computation, we can load one group of weights and the corresponding index. The index is used to load the group of input values to perform two MAC operations at the same time to generate the first temporary output. Then we can move to the next pair of weights and get the final output value. As shown here, by forcing the weights to be in aligned groups, the SIMD units can be fully utilized in the computation. Also, since each weight group is sharing the same index, the number of required column indexes can be dramatically reduced.

## Slide 11
SIMD-Aware Weight Pruning
0 | 0 | 6 | 4 | 0 | 1
2 | 0 | 0 | 3 | 5 | 7
0 | 1 | 2 | 0 | 8 | 0
8 | 0 | 4 | 3 | 0 | 0
0 | 0 | 0 | 0 | 0 | 2
5 | 9 | 1 | 0 | 0 | 1
Start with original weight matrix
Weights grouping
  Group size = SIMD width
0 | 0 | 6 | 4 | 0 | 1
2 | 0 | 0 | 3 | 5 | 7
0 | 1 | 2 | 0 | 8 | 0
8 | 0 | 4 | 3 | 0 | 0
0 | 0 | 0 | 0 | 0 | 2
5 | 9 | 1 | 0 | 0 | 1
Calculate importance of groups
  Root mean square
Remove redundant groups
  Importance < Threshold
 |  | 6 | 4 |  | 
 |  |  |  | 5 | 7
 |  |  |  | 8 | 0
8 | 0 | 4 | 3 |  | 
5 | 9 |  |  |  | 
Num of weights
Model size
Execution time
Notes: To ensure the weights in the sparse weight matrix are all in aligned groups, we propose SIMD-aware weight pruning. It starts with the original weight matrix. For the first step, weights are combined into groups with size equal to the SIMD width. Here we show the weights grouping with the SIMD width of 2. Then we need to calculate the importance of each weight group. We use root-mean-square value as the measurement of importance. In the last step, we can remove all the redundant groups with importance lower than the threshold. As shown in the figure, all the remaining weights are now in aligned groups. In this case, some unimportant weights need to be kept because the other weight in the same group is important. This will leads to an increase of remaining weights. However, because of the large reduction in column indexes, the entire model size can be further reduced. Also now the SIMD support can be fully utilized and it can help reduce the execution time.

## Slide 12
Chart: Pruning Rate
| 0.99 | 0.95 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3
dense | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Traditional Weight Pruning | 0.12048 | 0.25134 | 0.40666 | 0.6815 | 0.95791 | 1.2442 | 1.5141 | 1.7913 | 2.0689
SIMD-Aware Weight Pruning | 0.11973 | 0.19752 | 0.28629 | 0.4569 | 0.62982 | 0.80075 | 0.97349 | 1.1454 | 1.3184
Performance Benefit – Low Parallelism
ARM Cortex-M4 Microcontroller
68%
48%
Dense
Baseline
Notes: This figure shows the relative execution time of the sparse matrix multiplication with traditional weight pruning and SIMD-aware weight pruning. Those results are generated on the ARM Cortex-M4 microcontroller which is a low-parallelism hardware. The x-axis is the pruning rate which is the percentage of weights removed from the weight matrix. The y-axis is the relative execution time. The black line is the baseline with dense weight matrix. The blue line shows the relative execution time with traditional weight pruning. The cross point of the blue line and the baseline is around 68%, which means we need to remove more than 68% of the weights to achieve a reduction in execution time. The orange line shows the execution time with SIMD-aware weight pruning. The cross point decreases from 68% to 48%, which is a large gap. As shown in the figure, the DNN computation performance on low-parallelism hardware can benefit much from the SIMD-aware weight pruning.

## Slide 13
NVIDIA GTX Titan X
  Traditional weight pruning
Performance – High Parallelism
Chart: Pruning Rate
| 1.0 | 0.99 | 0.98 | 0.97 | 0.96 | 0.95 | 0.94 | 0.93 | 0.92 | 0.91 | 0.9
dense time | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
sparse time | 0.3514 | 0.64408 | 0.91237 | 1.0353 | 1.2386 | 1.4212 | 1.7819 | 1.9344 | 2.0905 | 2.1762
96.3%
Sparsity hurts performance
Pruning without sparsity
Dense
Baseline
Notes: However, things change much for high-parallelism hardware. This figure shows the relative execution time of sparse matrix multiplication on GPU with traditional weight pruning. The cross point here become 96.3%, which means we need to remove more than 96.3% of the weights in the weight matrix to get an execution time reduction. It is challenging for weight pruning to remove that much weights, which means the sparsity will hurt the computation performance. Therefore, we need to avoid sparsity during pruning to make sure that the DNN will not lose performance.

## Slide 14
Node Pruning
Remove redundant nodes
  Nodes: neurons (FC) / feature maps (CONV)
  Mask layers finds unimportant nodes
Add mask layers
Mask
Layer
Train mask layers
Remove redundant nodes and mask layers
Keep regular DNN structure: no sparsity
A
Notes: In this case, we propose the second technique named node pruning. To avoid sparsity during pruning, we need to keep the regular DNN structure. Therefore, node pruning remove the network redundancy by removing entire nodes instead of weights. Here nodes refer to the neurons in fully-connected layer and feature maps in the convolutional layers. By removing entire nodes, we will only reduce the size of each layer and will not break the regular DNN structure. In node pruning, we use mask layers to find unimportant nodes and, then remove them from the network. This figure shows a fully-connected layer. The first step of node pruning is adding mask layers. The output of the layer A need to go through the mask layer before propagating to the next layer. Each node in the mask layer has two parameters alpha and beta. For each DNN computation, if beta is lower than the threshold, alpha will be set to 0 and the output of the corresponding node will be blocked. Then we can train the parameter beta through normal DNN training procedure. As an example, after the training of mask layers, the third node in layer A is blocked, which means this node is actually redundant in the network. In the last step, we remove the redundant nodes and also the mask layers. Now layer A only has two nodes. The regular DNN structure is kept and there is no sparsity in the network.

## Slide 15
Combined Pruning – Moderate Parallelism
Chart: Pruning Rate
| 0.99 | 0.98 | 0.97 | 0.96 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
dense MKL | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SIMD-Aware Weight Pruning | 0.012768 | 0.018035 | 0.023032 | 0.028879 | 0.081115 | 0.19864 | 0.29441 | 0.39289 | 0.50499 | 0.61416 | 0.71281 | 0.79677 | 0.90167 | 1.0269
FC layers
CONV layers
Chart: Pruning Rate
| 1.0 | 0.99 | 0.98 | 0.95 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3
dense MKL | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SIMD-Aware Weight Pruning | 0.1545 | 0.22382 | 0.38641 | 0.66882 | 1.1973 | 1.759 | 2.2828 | 2.8344 | 3.3679 | 3.9127
SIMD-aware weight pruning
Node pruning
3%
84%
Dense
Dense
Intel Core i7-6700 CPU
Impact of sparsity on computation performance
Notes: For hardware with moderate parallelism, we will apply both the SIMD-aware weight pruning and node pruning. We first test the impact of the sparsity on computation performance. For fully-connected layers, this figure shows the relative execution time with SIMD-aware weight pruning. The x-axis is the pruning rate and the y-axis is the execution time. As shown in the figure, we only need to remove 3% of the weights to get an execution time reduction. Therefore, we will apply SIMD-aware weight pruning to the fully-connected layers. But for convolutional layers, the cross point is 84%. It is challenging to remove that much weights from convolutional layers. In this case, we should avoid sparsity and node pruning is applied.

## Slide 16
Evaluation Methodology
Networks
  MNIST: LeNet-300-100, LeNet-5
  CIFAR-10: ConvNet, Network-in-Network
  ImageNet: AlexNet
Hardware
  Low-parallelism: ARM Cortex-M4 microcontroller
  Moderate-parallelism: Intel Core i7-6700 CPU
  High-parallelism: NVIDIA GTX Titan X
Baseline: Traditional weight pruning *
* Han, Song, et al. "Learning both weights and connections for efficient neural network." NIPS. 2015.
Notes: For evaluation, we test scalpel on five networks on MNIST, CIFAR-10, and ImageNet. For hardware, we tested ARM Cortex-M4 microcontroller, Intel Core i7 CPU and Nvidia Titan X GPU as hardware platforms with low parallelism, moderate parallelism and high parallelism. For baseline, we will compare our results to the traditional weight pruning which removes weights with absolute value lower than a threshold.

## Slide 17
Chart: Relative Model Size
| LeNet-300-100 | LeNet-5 | ConvNet | NIN | AlexNet | geomean
Original | 1 | 1 | 1 | 1 | 1 | 1
Traditional | 0.093118 | 0.070774 | 0.48283 | 0.14708
Scalpel | 0.069294 | 0.06721 | 0.40946 | 0.12401
Chart: Relative Exec. Time
| LeNet-300-100 | LeNet-5 | ConvNet | NIN | AlexNet | geomean
Original | 1 | 1 | 1 | 1 | 1 | 1
Traditional | 0.16646 | 0.83762 | 1.0471 | 0.52657
Scalpel | 0.10902 | 0.28525 | 0.72636 | 0.28268
Results: ARM Cortex-M4 microcontroller
1.0
1.0
1.0
1.0
28% execution time
12% model size
Notes: This figure shows the relative execution time of the benchmarks on low-parallelism hardware. The blue bars are the original execution time. NIN and AlexNet are not tested since they have large model sizes that cannot fit on the microcontroller. The orange bars are the results of traditional weight pruning. The execution time of ConvNet actually increases after pruning. The green bars show the result of Scalpel. Compared to the traditional weight pruning, scalpel can achieve lower execution time on all benchmarks. On average, it can reduce the execution time to 28%. The next figure shows the relative model size after pruning. Scalpel can reduce the model size to 12%, which is lower than the traditional weight pruning.

## Slide 18
Chart: Relative Exec. Time
| LeNet-300-100 | LeNet-5 | ConvNet | NIN | AlexNet | geomean
Original | 1 | 1 | 1 | 1 | 1 | 1
Traditional | 0.26449 | 0.64721 | 1.2636 | 2.7077 | 1.2475 | 0.93917
Scalpel | 0.14582 | 0.24107 | 0.63281 | 0.81858 | 0.45358 | 0.38317
Results: Intel Core i7-6700 CPU
38% execution time
2.7
Chart: Relative Model Size
| LeNet-300-100 | LeNet-5 | ConvNet | NIN | AlexNet | geomean
Original | 1 | 1 | 1 | 1 | 1 | 1
Traditional | 0.093118 | 0.070774 | 0.48283 | 1.1852 | 0.22317 | 0.24267
Scalpel | 0.070804 | 0.051995 | 0.44282 | 0.81159 | 0.13059 | 0.17681
18% model size
Notes: For moderate-parallelism hardware, scalpel can reduce the execution time to 38%. At the same time, scalpel can reduce the model size to 18%, which is also better than traditional weight pruning.

## Slide 19
Chart: Relative Model Size
| LeNet-300-100 | LeNet-5 | ConvNet | NIN | AlexNet | geomean
Original | 1 | 1 | 1 | 1 | 1 | 1
Traditional | 0.093118 | 0.070774 | 0.48283 | 1.1852 | 0.22317 | 0.24267
Scalpel | 0.66828 | 0.11677 | 0.45399 | 0.81159 | 0.76522 | 0.46611
Chart: Relative Exec. Time
| LeNet-300-100 | LeNet-5 | ConvNet | NIN | AlexNet | geomean
Original | 1 | 1 | 1 | 1 | 1 | 1
Traditional | 0.80353 | 2.1151 | 3.6147 | 4.0477 | 3.3395 | 2.4202
Scalpel | 0.92167 | 0.62957 | 0.87862 | 0.85816 | 0.74334 | 0.79879
Results: NVIDIA GTX Titan X
80% execution time
47% model size
Notes: On high-parallelism hardware, scalpel reduces the execution time by 20%. However, for lenet-300-100, scalpel actually get higher execution time than the traditional weight pruning. One possible reason is that lenet-300-100 is too tiny that the computation cannot fit efficiently on Titan X. Therefore, although we can remove about 30% of the nodes from each layer, the execution time only decreases by 8.5%. For model size, scalpel can compress the DNN model to 47%. It is actually worse than the traditional weight pruning. This is because that scalpel is now pruning the network at a coarser granularity of nodes while the traditional weight pruning are still pruning individual weights.

## Slide 20
Conclusions
  Scalpel customizes pruning for hardware with different parallelism
  SIMD-aware weight pruning: utilizing SIMD units
  Node pruning: avoiding sparsity
  Microcontroller / CPU / GPU:
  Traditional: 53%, 94%, and 242% execution time
  Scalpel: 28%, 38%, and 80% execution time
  Traditional weight pruning has drawbacks
  Sparse format needs extra storage
  Execution time increase
Notes: In conclusion, we demonstrate that traditional weight pruning has many drawbacks. Extra storage needs to be spent on recording the sparse format. And the sparsity incurred by weight pruning will also lead to an execution time increase. To solve these problems, we propose scalpel. It customizes pruning for hardware with different parallelism. It consists of two techniques: SIMD-aware weight pruning and node pruning. On microcontroller, CPU and GPU, scalpel can reduce the execution time to 28%, 38% and 80%.

## Slide 21
Q & A
Notes: This is the end of the presentation. Thanks! I am happy to answer the questions.

## Slide 22
Thank you!

## Slide 23
Networks
Models | Num of Layers |  | Dataset | Error Rate
 | FC | CONV |  | 
LeNet-300-100 | 0 | 3 | MNIST | 1.50%
LeNet-5 | 2 | 2 |  | 0.68%
ConvNet | 3 | 1 | CIFAR-10 | 18.14%
Network-In-Network | 9 | 0 |  | 10.43%
AlexNet | 5 | 3 | ImageNet | 19.73% (top-5)

## Slide 24
Group Importance Measurement
Maximum absolute value (MAX)
Mean absolute value (MEAN)
Root-mean-square (RMS)
Chart: Pruning Rate of fc1 in LeNet-300-100
| 0.0 | 0.896573129251701 | 0.910229591836735 | 0.921624149659864 | 0.932610544217687 | 0.943877551020408 | 0.950229591836735 | 0.956913265306122 | 0.962159863945578 | 0.966173469387755 | 0.970331632653061 | 0.973656462585034 | 0.976198979591837 | 0.978392857142857 | 0.980059523809524 | 0.981777210884354 | 0.983613945578231 | 0.984897959183673
RMS | 0 | 0.04 | 0.04 | 0.06 | 0 | 0 | 0.03 | 0.07 | 0.01 | 0.03 | 0.04 | 0.01 | 0.05 | 0.02 | 0 | -0.06 | -0.13 | -0.2
MEAN | 0 | 0.01 | 0.02 | -0.01 | 0.08 | 0 | -0.05 | 0.01 | 0.08 | 0.04 | 0.06 | -0.04 | -0.05 | -0.05 | -0.07 | -0.19 | -1
MAX | 0 | 0.01 | 0.01 | 0.01 | 0.02 | -0.07 | 0 | 0.02 | -0.04 | -0.08 | -0.1 | -1
 | 0 | 0
98%
Notes: How to measure the group importance is critical to SIMD-aware weight pruning. We test three different measurements: maximum, mean absolute value and root mean square. We apply SIMD-aware weight pruning with different measurements to the first layer of LeNet-300-100. This figure shows the relative accuracy against the pruning rate. As you can see from the figure, RMS achieves the best pruning rate of 98% while keeping the original accuracy.

## Slide 25
Nodes Removed in Network-In-Network
Chart: 
| conv1 | cccp1 | cccp2 | conv2 | cccp3 | cccp4 | conv3 | cccp5 | cccp6
Remaining | 138 | 128 | 91 | 189 | 166 | 177 | 149 | 100 | 10
Removed | 54 | 32 | 5 | 3 | 26 | 15 | 43 | 92 | 0

## Slide 26
Chart: Relative Model Size
| LeNet-300-100 | LeNet-5 | ConvNet | NIN | AlexNet | geomean
Original | 1 | 1 | 1 | 1 | 1 | 1
Traditional | 0.093118 | 0.070774 | 0.48283 | 1.1852 | 0.22317 | 0.24267
Optimized | 0.093118 | 0.069905 | 0.475 | 1 | 0.22262 | 0.23311
Scalpel | 0.66828 | 0.11677 | 0.45399 | 0.81159 | 0.76522 | 0.46611
Chart: Relative Exec. Time
| LeNet-300-100 | LeNet-5 | ConvNet | NIN | AlexNet | geomean
Original | 1 | 1 | 1 | 1 | 1 | 1
Traditional | 0.80353 | 2.1151 | 3.6147 | 4.0477 | 3.3395 | 2.4202
Optimized | 0.80353 | 1.9005 | 2.7429 | 1 | 3.2005 | 1.6806
Scalpel | 0.92167 | 0.62957 | 0.87862 | 0.85816 | 0.74334 | 0.79879
Results: High Parallelism
80% execution time
47% model size
NVIDIA GTX Titan X
Notes: On high-parallelism hardware, scalpel reduces the execution time by 20%. However, for lenet-300-100, scalpel actually get higher execution time than the traditional weight pruning. One possible reason is that lenet-300-100 is too tiny that the computation cannot fit efficiently on Titan X. Therefore, although we can remove about 30% of the nodes from each layer, the execution time only decreases by 8.5%. For model size, scalpel compress the DNN model to 47%. It is actually worse than the traditional and optimized weight pruning. This is because that scalpel are now pruning the network at a coarser granularity of nodes while the traditional and optimized weight pruning are still pruning individual weights.

## Slide 27
Combined Pruning – Moderate Parallelism
Chart: Pruning Rate
| 0.99 | 0.98 | 0.97 | 0.96 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
dense MKL | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SIMD-Aware Weight Pruning | 0.012768 | 0.018035 | 0.023032 | 0.028879 | 0.081115 | 0.19864 | 0.29441 | 0.39289 | 0.50499 | 0.61416 | 0.71281 | 0.79677 | 0.90167 | 1.0269
FC layers
CONV layers
Chart: Pruning Rate
| 1.0 | 0.99 | 0.98 | 0.95 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3
dense MKL | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SIMD-Aware Weight Pruning | 0.1545 | 0.22382 | 0.38641 | 0.66882 | 1.1973 | 1.759 | 2.2828 | 2.8344 | 3.3679 | 3.9127
SIMD-aware weight pruning
Node pruning
3%
84%
Dense
Dense
Intel Core i7-6700 CPU
Impact of sparsity on computation performance
Notes: For hardware with moderate parallelism, we will apply both the SIMD-aware weight pruning and node pruning. For fully-connected layers, this figure shows the relative execution time after applying SIMD-aware weight pruning. The x-axis is the pruning rate and the y-axis is the execution time. As shown in the figure, we only need to remove 3% of the weights to get an execution time reduction. Therefore, we will apply SIMD-aware weight pruning to the fully-connected layers. But for convolutional layers, the cross point is 84%. It is impractical to remove that much weights from convolutional layers. In this case, we should avoid sparsity and node pruning is applied.

## Slide 28
Hardware Parallelism
Low parallelism - microcontroller
  No cache
  Low storage (~100 KB)
Moderate parallelism - desktop CPU
  ILP / MLP
  Deep cache hierarchy
  ~8 MB on-chip SRAM
High parallelism - GPU
  TLP
  High bandwidth / long latency memory
  2-12 GB storage
Notes: The first step of scalpel is analyzing hardware parallelism. We divide hardware into three categories. The first one is low-parallelism hardware, for example microcontrollers. It has no cache and only low storage. The second category is moderate-parallelism hardware like desktop CPUs. Instruction-level parallelism and memory-level parallelism are enabled. And they have a deep cache hierarchy. Hardware platforms like GPUs are considered as high-parallelism hardware. Thread-level parallelism is utilized, which requires a high bandwidth memory. They usually also have a large storage space.